## Slide 1: EnDev Indonesia PV-VP Troubleshooting Poster
A0 size poster (33.11 in x 46.81 in)
Landscape orientation
Full colour
Glossy paper, durable and weather resistant

## Slide 2
RESTARTING THE COMPUTER
Click the START button
Choose and click “Restart”
Click small white arrow for choices
1
2
3
Is there shading on the solar panels?
Computer display does not show correct information or error messages?
Is problem solved after computer restarted?
Are battery room and inverter room clean?
Sweep room, battery terminals and ventilation openings using broom and dry cloth only (no water!)
The RED light on inverter is ON?
Is “Low battery voltage” message displayed?
Are solar panels delivering sufficient energy
during the day?
No
Check circuit breaker at households and try reducing load
Reduce loads and use only priority devices
Are the solar panels clean?
Remove shade from trees and other obstructions
Clean panels from dust and other obstacles using water
No
Yes
Yes
Check Voltage (220 V) at all households connected on the same distribution branch
1. Check for broken cable and reconnect
2. Check for too many electricity connections
No
Is circuit breaker switch to households at power house ON?
Are battery and inverters operating well?
Turn circuit breaker switch ON
Circuit breaker switch switched OFF again?
No
Yes
1. Check for short circuited wiring
and
2. Check overload at customers and try reducing load
Yes
No
TROUBLESHOOTING AND MAINTENANCE GUIDE FOR VILLAGE SOLAR SYSTEMS
Yes
Yes
Yes
All customers
Some customers
One customer
Ask for Help
Technician name: ___________________________________________
Technician number: _________________________________________
Less than 220 V
Ask for Help
Technician name: ___________________________________________
Technician number: _________________________________________
220 V
Are there loose or broken cables?
Are any of the solar panels broken or show brown and white spots under the glass?
No
Ask for Help
Technician name: ___________________________________________
Technician number: _________________________________________
1. Check all cables at solar system
2. Switch off all loads until battery is fully recovered
Note: “Low battery voltage” indicates that battery is not sufficiently charged. Fully charging the battery may take a few days.
Check and fix electricity in one house
Unplug all devices and switch circuit breaker ON
Check voltage at main connection
Check voltage at all sockets
Plug on the devices (one by one)
Check circuit breaker - if trip then the device is shorted or the load is too high for one customer
Repeat from step 4 until broken devices known or max load identified
1) Before testing
2a) Good appliance
2b) Shorted appliance
Concept and design: Robert Schultz and Amalia Suryani | Technical advice: GOPA/Intec | ENDEV Indonesia © May 2013
“Overload” message shows on inverter display?
The RED light on charge controller is ON?
No
Yes
Yes
No
Restart the computer
Yes*
Check thin sensor cables for breakages and loose connections then repair
No
No electricity?
Overheating of battery room?
Monitoring system is not operating?
RED light on inverter or
charge controller?
Are any air ventilation openings blocked or obstructed?
Is the outside temperature very high?
Remove obstruction to improve air flow
Are there other heat sources in the room?
Idea: use a mobile electric fan to improve air flow in the battery room
Switch off or remove these sources of heat
Yes
No
Yes
Ask for Help
Technician name: ___________________________________________
Technician number: _________________________________________
Yes
Idea: if a battery room wall is exposed to much sun light, consider shading it using bamboo poles loosely leaned against the outside wall
Yes
- weekly maintenance actions
Are there loose or damaged cables underneath the solar panels?
Are there loose or damaged cables in the outside connection boxes?
Are there loose or damaged cables in cable trench to the battery house?
Reconnect, fix or reseal cables
Are there loose or damaged cables on the battery terminals?
Yes
Yes
Yes
No
No
No
Electrical Check
Yes
Yes*
Electrical Check
Yes
Is problem solved after checking and fixing electricity in affected house?
REMEMBER!
Sunny days ensure that the batteries are well charged
Cloudy days only provide little charge to the batteries
Rainy days provide no charge to the batteries
PV-VP Site Code: ___________________
Operator: __________ HP: ___________
Manager: __________ HP: ___________
Connected to: _______ households
Total PV capacity: _____ kWp
Total battery storage: _______ kWh
Total inverter capacity: ______ kW
Date commissioned: ____ /____ /____
No
No
5
4
3
2
1
“Error” ???
VILLAGE SOLAR SYSTEM COMPONENTS
Solar panels produce electricity from sunshine
2. Connection box combines cables from all solar panels
3. Charge controller protects the batteries
4. Batteries store electricity for night time use
5. Inverter converts solar electricity (DC) into grid electricity (AC)
2
1
3
4
5
6. Distribution grid connects to “load” (all electricity users)
6
5
Fix or reconnect the cables
Yes
* two actions are possible, try each until the problem solved
GENERAL GUIDANCE FOR ELECTRICAL SAFETY
Wear appropriate safety gear and take precautions
  Never work with electric parts before system is completely off
  Use gloves and wear shoes when dealing with cables and electricity even if the problem seems small and turn off switches
  Solar panels are ‘life’ when sunlight is present. Take extreme care not to cause short circuits in DC circuits, by connecting wrong wires
Use appropriate tools
Only work on the solar cables early morning or late afternoon when sunshine is limited
If operators cannot fix or find the problem by themselves contact trained technician only
Electrical Check
Check for RED light!
No

## Slide 3
RESTART KOMPUTER
1
2
3
Apakah ada bayangan lain pada panel surya?
Tampilan komputer tidak menunjukkan informasi yang benar atau pesan error?
Apakah masalah terselesaikan setelah restart komputer?
Apakah ruang baterai dan inverter bersih?
Sapu ruangan, terminal baterai dan bukaan ventilasi menggunakan sapu dan kain kering saja (tanpa air!)
Lampu MERAH pada inverter menyala?
Apakah pesan "tegangan baterai rendah“ ditampilkan?
Apakah panel surya memberikan energi yang cukup pada
siang hari?
Tidak
Periksa pemutus sirkuit (MCB) di rumah tangga dan coba kurangi beban
Kurangi beban dan gunakan hanya perangkat yang penting
Apakah panel surya bersih?
Singkirkan bayangan dari pepohonan dan penghalang lainnya
Bersihkan panel dari debu dan penghalang lain menggunakan air
Tidak
Ya
Ya
Periksa tegangan (220 V) pada semua pelanggan yang tersambung pada cabang distribusi yang sama
Tidak
Ya
Ya
Semua pelanggan
Beberapa pelanggan
Satu pelanggan
Minta Bantuan
Nama teknisi: ______________________________________________
Nomor telepon teknisi: ______________________________________
Apakah ada panel surya yang rusak atau menunjukkan bintik-bintik coklat dan putih di bawah kaca?
Tidak
Minta Bantuan
Nama teknisi: ______________________________________________
Nomor telepon teknisi: ______________________________________
1. Periksa semua kabel di PLTS
2. Matikan semua beban sampai baterai benar-benar pulih
Catatan: “Tegangan baterai rendah" menunjukkan baterai yang tidak terisi cukup. Pengisian penuh baterai mungkin memakan waktu beberapa hari.
Memeriksa dan memperbaiki listrik di satu rumah
Lepas kabel semua alat dan nyalakan saklar pemutus sirkuit (CB)
Periksa tegangan pada sambungan utama
Periksa tegangan pada semua stop-kontak
Nyalakan alat-alat (satu demi satu)
Periksa saklar CB - jika turun maka alat korslet atau beban terlalu tinggi untuk satu pelanggan
Ulangi dari langkah 4, sampai peralatan yang rusak ditemukan atau beban maksimum diketahui
1) Sebelum tes
2a) Alat baik
2b) Alat korslet
Konsep dan desain: Robert Schultz dan Amalia Suryani | Saran teknis: GOPA/Intec | ENDEV Indonesia © Mei 2013
Pesan “kelebihan beban" muncul pada tampilan inverter?
Lampu MERAH pada charge controller menyala?
Tidak
Ya
Ya
Tidak
Restart komputer
Ya*
Periksa kabel sensor tipis untuk kerusakan dan koneksi longgar lalu perbaiki
Tidak
Tidak ada listrik?
Ruang baterai terlalu panas?
Sistem pemantauan tidak beroperasi?
Apakah ada bukaan ventilasi udara yang terhalang atau terhambat?
Apakah suhu di luar sangat tinggi?
Hilangkan hambatan untuk memperbaiki aliran udara
Apakah ada sumber panas lain di ruangan itu?
Ide: gunakan kipas angin listrik untuk memperbaiki aliran udara di ruang baterai
Matikan atau singkirkan sumber-sumber panas
Ya
Tidak
Ya
Minta Bantuan
Nama teknisi: ______________________________________________
Nomor telepon teknisi: ______________________________________
Ya
Ide: jika dinding ruang baterai terkena banyak cahaya matahari, pertimbangkan membuat bayangan menggunakan tiang bambu yang bersandar dengan longgar di dinding luar
Ya
- cara perawatan mingguan
Apakah ada kabel yang longgar atau rusak di bawah panel surya?
Apakah ada kabel yang longgar atau rusak di di luar kotak koneksi?
Apakah ada kabel yang longgar atau rusak di parit kabel ke rumah baterai?
Sambungkan kembali, perbaiki, atau tutup kembali kabel
Apakah ada kabel yang longgar atau rusak pada
Ya
Ya
Ya
Tidak
Tidak
Tidak
Ya
Ya*
Pemeriksaan Listrik
Ya
Apakah masalah terselesaikan setelah memeriksa dan memperbaiki listrik di rumah tersebut?
INGAT!
Hari-hari cerah memastikan bahwa baterai diisi dengan baik
Hari-hari berawan hanya mengisi sedikit baterai
Hari-hari dengan hujan tidak bisa mengisi baterai
Kode lokasi PLTS: ___________________
Operator: __________ HP: ___________
Manajer: __________ HP: ___________
Tersambung ke: _______ KK
Kapasitas PV total: _____ kWp
Penyimpanan baterai total: _______ kWh
Kapasitas inverter total: ______ kW
Tanggal komisioning: ____ /____ /____
Tidak
Tidak
5
4
3
2
1
“Error”???
KOMPONEN PLTS TERPUSAT
Panel surya menghasilkan listrik dari sinar matahari
2. Kotak koneksi menggabungkan kabel dari semua panel surya
3. Charge controller melindungi baterai
4. Baterai menyimpan listrik untuk penggunaan di malam hari
5. Inverter mengkonversi listrik tenaga surya (DC) ke listrik jaringan (AC)
2
1
3
4
5
6. Jaringan distribusi menghubungkan ke “beban” (semua pelanggan listrik)
6
5
* mungkin ada dua aksi, coba masing-masing sampai masalah terpecahkan
Lampu MERAH pada inverter atau charge controller?
Pemeriksaan Listrik
Klik tombol START
Pilih dan klik “Restart”
Klik panah putih kecil untuk pilihan
PEDOMAN UMUM UNTUK KESELAMATAN LISTRIK
Kenakan perlengkapan keselamatan yang tepat dan lakukan tindakan pencegahan
Jangan bekerja dengan listrik sebelum sistem sepenuhnya mati
  Gunakan sarung tangan dan kenakan sepatu ketika berurusan dengan kabel dan listrik walaupun masalah terlihat sepele dan matikan saklar
  Panel surya ‘hidup’ ketika ada cahaya matahari. Sangat berhati-hatilah untuk tidak menyebabkan korslet/arus pendek di sirkuit DC, dengan menghubungkan kabel yang salah
Gunakan alat yang tepat
Hanya bekerja pada kabel surya pada pagi atau sore hari saat sinar matahari terbatas
Jika operator tidak dapat memperbaiki atau menemukan masalah sendiri hubungi teknisi terlatih
Pemeriksaan Listrik
Periksa apakah ada kabel yang putus dan sambungkan kembali
Periksa apakah ada terlalu banyak sambungan pelanggan
Apakah saklar pemutus sirkuit (CB) ke pelanggan yang ada di rumah pembangkit menyala?
Apakah baterai dan inverter beroperasi dengan baik?
Nyalakan saklar pemutus sirkuit (CB)
Apakah saklar pemutus sirkuit (CB) mati lagi?
Tidak
Ya
1. Periksa apakah ada kabel yang korslet/arus pendek
dan
2. Periksa kelebihan beban pelanggan dan coba kurangi beban
Ya
Tidak
Ya
Kurang dari 220 V
Minta Bantuan
Technician name: ___________________________________________
Technician number: _________________________________________
220 V
Apakah ada kabel yang longgar atau rusak?
Perbaiki atau sambungkan kembali kabel
Ya
Periksa lampu MERAH!
Tidak
PANDUAN PERAWATAN DAN PEMECAHAN PERMASALAHAN PLTS TERPUSAT